## Slide 1: Blood Spillage Mercury Spillage
Dr. Sapna Patel 3rd Year Resident Doctor, Biochemistry Department, Government Medical College, Bhavnagar.

## Slide 2: Blood spillage policy
Risk of disease transmission to laboratory workers.
Blood spillage may occur due to
  laboratory sample breaks in the phlebotomy area
  during transport of clinical sample
  excessive bleeding during the procedure.

## Slide 3: How to handle Blood or body fluid spillage?
Wear PPE
Evacuate the area

## Slide 4: How to handle Blood or body fluid spillage?
Isolate the spill area
Use brush to sweep up of broken glass.
Do not pick up pieces with your hands.

## Slide 5: Procedure to Manage Blood Spillage
Absorb blood or body fluids using newspaper, blotting paper / paper towel

## Slide 6
Take freshly prepared 1 % sodium hypochlorite.
- Preparing hypochlorite solution
- dilution 1:4
- For 1 liter solution,
200ml sodium hypochlorite +
800ml water
Commercially 4-5 % HOCL is available
  Pore 1 % HOCL on spillage area and keep it for 20 minute with “CAUTION BOARD”
Procedure to prepare 5% sodium hypochlorite

## Slide 7
Spray the hypochlorite and leave for
30 minutes

## Slide 8
After it take the blood
absorbed towel/cotton and discard in yellow container
Procedure to Manage Blood Spillage

## Slide 9: Procedure to Manage Blood Spillage
Remove gloves and discard them.
Wash hands carefully with soap and water.

## Slide 10: How to handle Blood or body fluid spillage?
Use of Mercury :-
Dental amalgam
Thermometer
Sphygmomanometer
Preservative in some vaccines
Reagents

## Slide 12: Component of mercury spillage kit:-
Mercury absorbent
Safety goggles
Latex gloves
Lab coat
Mercury cleanup wipes
Dust pan
Disposal bag

## Slide 14: How to handle mercury spillage?
Wear rubber or latex gloves & PPE.
Switch off the fan
Broken glass piece
  Big glass with rubber brush & plastic Supadi.
  Small glass pick with forceps
Put in paper towel
Fold it & place in zip locking bag.(label it)
Use a rubber brush to gather mercury beads.
Place it in a zip locking bag.(label it)
If possible clean the area with 20% calcium sulfide or sodium thiosulfate.
Gloves used during process also sent with bag.

## Slide 15: Process of cleaning mercury spillage:-
Remove the broken thermometer
wrap broken thermometer
dispose as per BMW rule.
Collect the mercury globules together with the scoope
Using the syringe, pick up a mercury and place it in waste plastic bottle.

## Slide 16: Process of cleaning mercury spillage:-
Cover the spillage area with powder
  calcium hydroxide
  sulpher
By using scoope, mix powder with spilt mercury.
Brush the contaminated powder into the scoope and place it into waste container
And cap the container tightly and can be kept safely.
Dispose of waste material in the incineration waste stream.

## Slide 17: Questions
Que 1. Content of universal spill kit
Que 2. Hypo chloride solution should be left for how many duration?
Que 3. Which protective equipment should be wear by the staff cleaning the spill?
Que 4. Which is the best way to prevent spill?
Que 5. Name the infections transmitted by blood or other body fluids.
Que 6. Common source of mercury in biochemistry laboratory.
Que 7. what is the first step in spill management?

## Slide 18
THANK YOU

## Slide 19
Spillage of chemical on skin or eye

## Slide 20
Hazard of Mercury:-
Nervous system
  Irritability
  Memory problems
  Confusion – delirium
  Muscle weakness
  Numbness
  Hearing and speech difficulties
Digestive system
  Peptic ulcer
  Peptic perforation
Respiratory systems
  Mergury fume - breathlessness
Threat to the development of the child in utero